## Slide 1: Governor
Adam Rakun & Matteo D’Urso
Embedded Systems (5063EMSY6Y)
A. Pathania, H. Xu

## Slide 2: Index
Overall Structure
Design-Time: Look-Up table
Run-Time: MIMO PID-Controller
PID Controller
PID Decisions
Power Estimation Model

## Slide 3: Overall structure
Design-Time component
  Look-Up table for a fixed component order, and partition points.
Run-Time component
  MIMO PID controllers
    DVFS
    Partition points

## Slide 4: Design-Time: Look-Up table
Matrix that contains all (TP, Latency) pairs of a G-B-L, 4-6 pipeline.
All entries compared against target TP and Latency → choose configuration with lowest error.
Assumption: given that this is overall an efficient pipeline, the optimal solution will be close to this solution.

## Slide 5: Run-Time: MIMO PID-Controller
MIMO PID → 2 nested PIDs
  Partition points → Latency, TP
  DVFS → Latency, TP
constrained optimization problem: minimize power consumption while meeting TP and latency targets
Model-free variation: because few data → bad model
Heavily relies on power estimation model

## Slide 6: PID Controller

## Slide 7: PID Decisions
Inputs per iteration
- Targets: target_fps, target_latency
- Measurements: fps, latency, stage times T1/T2/T3
Normalized error signals
- fps_error = (target_fps − fps) / target_fps
- lat_error = (latency − target_latency) / target_latency
Decision layer
- If any constraint violated → Feasibility mode
                > Run PID update for violated metrics
      > Apply frequency adjustment (clamped to valid DVFS steps)
      > If frequencies saturated / unstable → adjust partitions using bottleneck stage
- If both constraints met → Power-reduce mode
  > Compute margins (FPS slack, latency slack)
  > Reduce power with small steps (DVFS first, then partitions if safe)
Bottleneck-aware partitioning
- Throughput dominated by max(T1, T2, T3)
- Shift work away from bottleneck component (avoid 1-layer stages)

## Slide 8: Power Estimation Model
Simple rule derived from measurements
  Calculate a workload fraction for a specific component:
    weighted_frac = frac_layers * alexnet_layer_computation_load
  CPUs: power(cpu) = weighted_frac(cpu) * fx_power(cpu)
  GPUs: power(gpu) = weighted_frac(gpu) * POWER_GPU
  Overhead:
    (big_cpu_freq * big_cpu_overhead +
    little_cpu_freq * little_cpu_overhead) * scale_factor
*: found by experiments *: found by trial and error